| STLC/TTLC Regulatory Limits |
| --- |
| Soluble Threshold Limit Concentration (STLC) and Total Threshold Limit Concentration (TTLC) Regulatory Limits* |
|  | Organic Substances | STLC Level (mg/L) | TTLC Level (mg/Kg - wet weight) |  |
|  | Aldrin | 0.14 | 1.4 |  |
|  | Chlrodane | 0.25 | 2.5 |  |
|  | DDT, DDE, DDD | 0.1 | 1 |  |
|  | 2,4-Dichlorophenoxyacetic acid | 10 | 100 |  |
|  | Dieldrin | 0.8 | 8 |  |
|  | Dioxin (2,3,7,8-TCDD) | 0.001 | 0.01 |  |
|  | Endrin | 0.02 | 0.2 |  |
|  | Heptachlor | 0.47 | 4.7 |  |
|  | Kepone | 2.1 | 21 |  |
|  | Lead compounds, organic | - | 13 |  |
|  | Lindane (gamma-BHC) | 0.4 | 4 |  |
|  | Methoxychlor | 10 | 100 |  |
|  | Mirex | 2.1 | 21 |  |
|  | Pentachlorophenol | 1.7 | 17 |  |
|  | PCBs (Polychlorinated Biphenyls) | 5.0 | 50 |  |
|  | Toxaphene | 0.5 | 5 |  |
|  | Trichloroethylene | 204 | 2040 |  |
|  | 2,4,-Trichlorophenoxypropionic acid | 1.0 | 10 |  |
|  | * Used for California regulated hazardous waste. Source is California Code of Regulations, Title 22, Chapter 11, Article 3. |
| STLC/TTLC Regulatory Limits |
| Soluble Threshold Limit Concentration (STLC) and Total Threshold Limit Concentration (TTLC) Regulatory Limits* |
|  | Inorganic Substances | STLC** Level (mg/L) | TTLC*** Level (mg/Kg - wet weight) |  |
|  | Antimony (and/or Sb compounds) | 15 | 500 |  |
|  | Arsenic (and/or As compounds) | 5 | 50 |  |
|  | Asbestos | - | 1% |  |
|  | Barium (and/or Ba compounds) | 100 | 10000**** |  |
|  | Beryllium (and/or Be compounds) | 0.75 | 75 |  |
|  | Cadmium (and/or Cd compounds) | 1 | 100 |  |
|  | Chromium VI compounds | 5 | 500 |  |
|  | Chromium (and/or Cr III compounds) | 5***** | 2500 |  |
|  | Cobalt (and/or Co compounds) | 80 | 8000 |  |
|  | Copper (and/or Cu compounds) | 25 | 2500 |  |
|  | Fluoride salts | 180 | 18000 |  |
|  | Lead (and/or Pb compounds) | 5 | 1000 |  |
|  | Mercury (and/or Hg compounds) | 0.2 | 20 |  |
|  | Molybdenum (and/or Mo compounds) | 350 | 3500 |  |
|  | Nickel (and/or Ni compounds) | 20.0 | 2000 |  |
|  | Selenium (and/or Se compounds) | 1 | 100 |  |
|  | Silver (and/or Ag compounds) | 5 | 500 |  |
|  | Thallium (and/or Tl compounds) | 7.0 | 700 |  |
|  | Vanadium (and/or V compounds) | 24 | 2400 |  |
|  | Zinc (and/or Zn compounds) | 250 | 5000 |  |
|  | * Used for California regulated hazardous waste. Source is California Code of Regulations, Title 22, Chapter 11, Article 3. |
|  | ** If a substance is ten times (by rule of thumb) the STLC value found on the TTLC, the Waste Extraction test (WET) should be used. If any substance in the waste so analyze equals or exceeds the STLC value, it is considered a hazardous toxic waste. |
|  | ***If a substance in a waste equals or exceeds the TTLC level, it is considered a hazardous toxic waste. |
|  | **** Excludes barium Sulfate |  |  |  |
|  | ***** If the soluble chromium as determined by the TCLP is less than 5mg/L, and the soluble chromium as determined by the STLC test equals or exceeds 560mg/L, and the waste is not otherwise identified as a RCRA hazardous waste, then the waste is a non-RCRA hazardous waste. |