| ORGANICS |  |  |  |
| --- | --- | --- | --- |
| Water/Liquid |  |  |  |
| Parameter | Container (with Teflon lined lid) | Preservative | Holding Time |
| Volatile Organics | 40ml VOA vial | Cool to 4 degrees C HCl to pH 2* | 14 days |
| Base Neutrals/ Acid Extractable | 1 L Amber glass | Cool to 4 degrees C | 7 days to extract |
| Pesticides/PCBs | 1 L Amber glass | Cool to 4 degrees C | 7 days to extract |
| Phenols (Acids) | 1 L Amber glass | Cool to 4 degrees C | 7 days to extract |
| TPH Extractable (Diesel/Oil) | 1 L Amber glass | Cool to 4 degrees C | 7 days to extract |
| Purgeable Halocarbons | 40ml VOA vial | Cool to 4 degrees C HCl to pH 2* | 14 days |
| Purgeable Aromatic Hydrocarbons | 40ml VOA vial | Cool to 4 degrees C HCl to pH 2* | 14 days |
| Acrolein and Acrylonitrile | 40ml VOA vial | Cool to 4 degrees C HCl to pH 2** | 14 days |
| TPHg/BTEX | 40ml VOA vial | Cool to 4 degrees C HCl to pH 2* | 14 days |
| Total Organic Halogens | 500 ml Amber glass | Cool to 4 degrees C | 14 days |
| Herbicides | 1L Amber glass | Cool to 4 degrees C | 7 days to extract |
| * Exempt if samples analyzed within 7 days |  |  |
| ** pH adjustment only required for Acrylonitrile |  |  |
| INORGANICS |  |  |  |
| Parameter | Container | Preservative | Holding Time |
| Acidity | 100 ml P/G | Cool to 4 degrees C | 14 days |
| Alkalinity | 100 ml P/G | Cool to 4 degrees C | 14 days |
| Ammonia - Nitrogen | 100 ml P/G | Cool to 4 degrees C | 28 days |
| Biochemical Oxygen Demand | 500 ml P/G | Cool to 4 degrees C | 48 hours |
| Bromide | 250 ml P/G | None required | 28 days |
| Chemical Oxygen Demand | 100 ml P/G | Cool to 4 degrees C H2SO4 to pH 2 | 28 days |
| Chloride | 200 ml P/G | None required | 28 days |
| Chlorine Residual | 100 ml P/G | None required | 15 minutes |
| Color | 100 ml P/G | Cool to 4 degrees C | 48 hours |
| Cyanide | 100 ml P/G | Cool to 4 degrees C NaOH to pH >12 | 14 days |
| Fluoride | 100 ml P/G | None required | 28 days |
| Hardness | 100 ml P/G | PH <2 with NHO3 or H2SO4 | 6 months |
| Metals | 500 ml P/G | HNO3 to pH <2 | 6 months |
| Cr (VI) | 500 ml P/G | Cool to 4 degrees C | 24 hours |
| Mercury | 500 ml P/G | HNO3 to pH <2 | 28 days |
| Nitrogen (TKN) | 500 ml P/G | H2SO4 to pH <2 | 6 months |
| Nitrate - Nitrogen | 100 ml P/G | Cool to 4 degrees C | 48 hours |
| Oil & Grease | 1 L. G | Cool to 4 degrees C | 28 days |
| Total Organic Carbon | 100 ml P/G | Cool to 4 degrees C/pH <2 with H2S | 28 days |
| Orthophosphate | 100 ml P/G | Filter immediately | 48 hours |
| Oxygen (Dissolved) | N/A | None required | 15 minutes |
| Phenolics, total | 1 qt. G only | Cool to 4 degrees C/pH <2 with H2S | 28 days |
| Phosphorus, total | 100 ml G only | Cool to 4 degrees C/pH <2 with H2SO4 | 28 days |
| Solids (Volatile, Suspended, Total, Dissolved) | 100 ml P/G each | Cool to 4 degrees C | 7 days |
| Temperature | N/A | None required | Analyze immediately |

P = Plastic   G = Glass